## Slide 1
5/20 Progress Report
Presenter: I-An Hou
PPU with Approx. Softmax and Testbench

## Slide 2: Modification
Error occur in quantization part, other parts function normally.

## Slide 3: Modification
It was simply a problem about matching output clock cycles together.

## Slide 4: Modification
The scaling module is modified to support FP8 multiplication.
FP8 definition is (E4M3 format) :
1 bit
4 bit
3 bit

## Slide 5: Modification
First part is decoding FP8 format.
Then transferring it to Q8.8 fixed point number. But why Q8.8 ?
The output bit width for each mac is 40 bits, which is 40 – 24 = 16 bits wider. Since Q8.8 is 16 bits wide, the result is 24 + 16 + 16 – 16 = 40.

## Slide 6: Modification
Testcase: Mimicking mac unit multiplying (70, 80) and (40, 90)
Quantized int4 data: (6, 7), (3, 7)
CS: 0.101237 = 0x1D in FP8
VSs: 113, 127.
Output of mac should be (6 * 3 + 7 * 7) * 113 * 127 = 961517
*Theoretical output = 2800 + 7200 = 10000
*CS = coarse-grain scale factor
VSs = per vector scale factors

## Slide 7: Approx. Softmax
Normal softmax:
Approximate softmax:
Use 2 as base instead of e, hence replacing exponential calculations with shifting.

## Slide 8: Approx. Softmax
The reference didn’t specify the bit width after approx. softmax, so I assume it to be 8 (common).
So the maximum shift amount is set to be 7.

## Slide 9: Approx. Softmax
In the division state, each value is multiplied by 255 before the division to map the result to 8 bits.

## Slide 10: Testing Correctness
The test case is (120, 120, 121, 121, … , 127, 127), the theoretical output is
The Verilog code output is
Correct.