## Slide 1
5/27 Progress Report
Presenter: I-An Hou
Overall Modification, Layout and Post Sims

## Slide 2: Progress Report
Put MAC, ACC collector, and PPU together successfully
Currently working on synthesis

## Slide 3: Block Diagram
The whole accelerator is consist of MAC units, accumulation collector, and a PPU.
MAC UNITS
ACC COLLECTOR
PPU
Partial_sum_out
Partial_sum_in
to_ppu
a_vec, b_vec, mode
valid_ppu
quantized_data
softmax_data
valid_ppu

## Slide 4: Modification
Old design: large FSM in control unit

## Slide 5: Modification
Modified: simplified FSM in MAC and accumulation collector
IDLE
CALC
valid
calc_count == calc_max
IDLE
MAC
PPU
start
ppu
addr == 15
(output complete)
MAC
ACC

## Slide 6: Testbench
Testcase: (0, 1, 2, 3, … , 31) + scale (scale = 0 in int8 mode)
Total number of input = 32
One of the input is modified to be much smaller
Scale = 0x65, bias = 1
32

## Slide 7: Testbench
Normal scaled sum: in Q8.8 = 56329728
Small scaled sum: in Q8.8 = 46903584

## Slide 8: Testbench
Max = 56329728 =3, reciprocal = 255 << 6 / 3 = 5440

## Slide 9: Synthesis
.tcl, .sdc, .setup files: from DSD lecture
Library used: /home/raid7_2/course/cvsd/CBDK_IC_Contest/CIC/SynopsysDC/db/typical.db
The area is huge, still optimizing it.

## Slide 10: Synthesis
Optimizing each MAC: adder tree

## Slide 11: Synthesis
Optimizing each MAC: adder tree