## Slide 1: PPU and Testbench
5/6 Progress Report
Presenter: I-An Hou

## Slide 2: Recall
Scaling, biasing
ReLU
Truncation
Max, reciprocal
Quantization

## Slide 3: Input, Output Ports
vec_max_wire and reciprocal_wire are for debug

## Slide 4: Scaling and Biasing
Each result of MAC times scale and padding to 40 bits. (40 * 16 banks = 640 bits as mentioned in the paper)

## Slide 5: ReLU
If the scaled and biased result is negative, cover it with 0.

## Slide 6: Truncation
Pick the high 18 bits to be the truncated result, and add 8 bits to reach 296 bits as mentioned in the paper.

## Slide 7: Truncation
Pick the high 18 bits to be the truncated result, and add 8 bits to reach 296 bits as mentioned in the paper.

## Slide 8: Latch Array

## Slide 9: Finite State Machine of Latch Array
IDLE
INPUT
OUTPUT
Doing nothing, all registers store their values.
Writing latch array with data after ReLU.
Reading datas in latch array.

## Slide 10: Finite State Machine of Latch Array
IDLE
INPUT
OUTPUT
When Quantizing
Done or reset
Reset

## Slide 11: Vector Max
When in “OUTPUT” mode, find the max value in latch array.

## Slide 12: Reciprocal
When the maximal value is determined, calculate the scale factor
Because scale factor is usually small, shift the answer left by 13 bits to prevent vanishing.

## Slide 13: Quantization and Rounding
After switching to OUTPUT mode, quantize each data in latch array and store the result in a buffer implemented in testbench. (Remember to >> 13)

## Slide 14: Testbench
Partial sum for the input is
{0110000…0, 8{0100000…0}, 0111110…0, 5{0100000…0}, 0111000…0}
Scale = 16, Bias = 1

## Slide 15: Current Progress
Error occur in quantization part, other parts function normally.